## Slide 1: Introduction to the Internet of Things and Embedded Systems Introduction to 4IR, Internet of Things and Embedded Systems
Notes: Sources:
https://www.edx.org/course/getting-started-with-the-internet-of-things-iot-2
https://www.coursera.org/learn/iot
And many other sources.

## Slide 3: What is the Fourth Industrial Revolution?
Klaus Schwab, founder and executive chairman of the Geneva-based WEF, published a book in 2016 titled "The Fourth Industrial Revolution" and coined the term at the Davos meeting that year.
Schwab argued a technological revolution is underway "that is blurring the lines between the physical, digital and biological spheres."
Simply put, the Fourth Industrial Revolution refers to how technologies like artificial intelligence, autonomous vehicles and the internet of things are merging with humans' physical lives. Think of voice-activated assistants, facial ID recognition or digital health-care sensors.
Schwab argued these technological changes are drastically altering how individuals, companies and governments operate, ultimately leading to a societal transformation similar to previous industrial revolutions.
Notes: Klaus Schwab, founder and executive chairman of the Geneva-based WEF, published a book in 2016 titled "The Fourth Industrial Revolution" and coined the term at the Davos meeting that year.
Schwab argued a technological revolution is underway "that is blurring the lines between the physical, digital and biological spheres."
Simply put, the Fourth Industrial Revolution refers to how technologies like artificial intelligence, autonomous vehicles and the internet of things are merging with humans' physical lives. Think of voice-activated assistants, facial ID recognition or digital health-care sensors.
Schwab argued these technological changes are drastically altering how individuals, companies and governments operate, ultimately leading to a societal transformation similar to previous industrial revolutions.

## Slide 4: The first three industrial revolutions
Zvika Krieger, the head of technology policy and partnerships at WEF, told CNBC that there is a common theme among each of the industrial revolutions: the invention of a specific technology that changed society fundamentally.
The First Industrial Revolution started in Britain around 1760. It was powered by a major invention: the steam engine. The steam engine enabled new manufacturing processes, leading to the creation of factories.
The Second Industrial Revolution came roughly one century later and was characterized by mass production in new industries like steel, oil and electricity. The light bulb, telephone and internal combustion engine were some of the key inventions of this era.
The inventions of the semiconductor, personal computer and the internet marked the Third Industrial Revolution starting in the 1960s. This is also referred to as the "Digital Revolution."

## Slide 5: Difference between Third and Fourth
Fourth Industrial Revolution is different from the third for two reasons: the gap between the digital, physical and biological worlds is shrinking, and technology is changing faster than ever.
For evidence of how quickly technological change is spreading, observe the adoption of the telephone. It took 75 years for 100 million people to get access to the telephone; the gaming app "Pokemon Go" hooked that many users in less than one month in 2016.

## Slide 6: The Issues and Concerns
Some experts warn of a "winner-take-all economy," where high-skilled workers are rewarded with high pay, and the rest of workers are left behind.
A 2018 report by investment firm UBS found billionaires have driven almost 80 percent of the 40 main breakthrough innovations over the past four decades.
In 2016, Schwab predicted inequality would be the greatest societal concern associated with the Fourth Industrial Revolution.
"There has never been a time of greater promise, or one of greater potential peril"

## Slide 8: We are Way Behind the Developed Countries

## Slide 9: We have Adopted Leapfrog Strategy for Pakistan
Andrew Ng has proposed a brilliant strategy for developing countries that have fallen behind in the technology race.
The idea is to skip over the intermediary technologies and leapfrog into the future by adopting 4IR technologies.
With this approach, it is possible to achieve exponential growth in a shorter period of time.
Notes: Andrew Ng (https://www.andrewng.org) is a Chinese English computer scientist, executive, investor, and entrepreneur, who co-founded and led Google Brain team and also was a VP & Chief Scientist at Baidu and currently he is an adjunct professor at Stanford University.

## Slide 10: The Internet of Things (IoT) will power the Fourth Industrial Revolution
The Fourth Industrial Revolution is changing the very software-defined automation allows manufacturers to link all stages of the value chain, rapidly adapt to changing markets, and create highly personalised products on a mass scale.
The opportunities presented by this revolution are incredible. According to McKinsey, the economic impact of smart factories could reach up to $2.3 trillion per year by 2025.
At the heart of the Fourth Industrial Revolution is the Internet of Things (IoT), which uses digital technology to connect sensors, actuators, and machines to each other and to factory workers.
Notes: https://www.intel.com/content/dam/www/public/us/en/documents/white-papers/fourth-industrial-revolution-white-paper.pdf
https://www.weforum.org/agenda/2017/06/internet-of-things-will-power-the-fourth-industrial-revolution/
https://www.zdnet.com/article/how-iot-will-drive-the-fourth-industrial-revolution/

## Slide 11: What is IoT?
The Internet of Things, or IoT, refers to the billions of physical devices around the world that are now connected to the internet, collecting, sharing and analyses of data.
Thanks to cheap processors and wireless networks, it's possible to turn anything, from a pill to an aeroplane to a self-driving car into part of the IoT

## Slide 12: Definition
The Internet of Things is the network of physical devices that combine IP connectivity with software, sensors, actuators, and other electronics to directly integrate the physical world into our computer-based systems, resulting in efficiency improvements and economic benefits.
Simpler Definition:
The Internet of Things is a network of Internet connected devices that communicate embedded sensor data to the cloud for centralized processing.

## Slide 13: IoT is about Billions of Devices
The Internet of Things, or IoT, refers to the billions of physical devices around the world that are now connected to the internet, collecting, sharing and analyses of data.
Thanks to cheap processors and wireless networks, it's possible to turn anything, from a pill to an aeroplane to a self-driving car into part of the IoT

## Slide 14: The Current and Future Impact of IoT
The IEEE has compiled data and makes the following claims about its current and future impact:
In 2015, the global wearables market had already increased 223% from the previous year (and data on Statista shows it increasing by another 243% between 2015 and 2022)
By 2020, 250 million vehicles were connected to the Internet
IoT will add 15 trillion dollars to the global economy over the next 20 years
There will be 50 billion Internet-connected devices by the year 2020.
Notes: As the market becomes more mature, these figures will no doubt change but the current trend looks as if IoT is not only here to stay but positioned to make a substantial impact both socially, in business, and economically.
[^1]: Source: https://www.comsoc.org/blog/infographic-internet-things-iot
[^2]: Source: https://www.statista.com/statistics/437871/wearables-worldwide-shipments/

## Slide 15: Benefits of IoT
The interconnection of these multiple embedded devices will be resulting in automation in nearly all fields and also enabling advanced applications. This is resulting in improved accuracy, efficiency and economic benefit with reduced human intervention. The major benefits of IoT are:
Improved Customer Engagement
Technical Optimization
Reduced Wastage
Integrate and Adapt Business Model
Better Business Decision

## Slide 16: End-to-end IoT

## Slide 17: Example IoT Devices

## Slide 18: Applications of IoT

## Slide 19: Introduction to IoT

## Slide 20: Value Proposition

## Slide 21: Layers of IoT

## Slide 22: Challenges to IoT

## Slide 23: Past, Present and Future of IoT

## Slide 24: What are Embedded Systems?
IoT devices are embedded systems
Computer based Systems that do not appear to be computers - complexity is hidden from the users
The complexity is embedded inside the device (that is where the name came from)
IoT devices are always connected to the internet
Embedded systems may have computational complexity but may or may not be connected to a network
Things are moving from Embedded to IoT, a lot of thing were Embedded but are now IoT
Sometime an Embedded System does not interact with the user but with another system, invisible to the user (Disk drive, anti lock braking system)
Notes: Watch 04 What are Embedded Systems

## Slide 25: Efficiency Rules in Embedded Systems
Most embedded systems are in cost-critical markets (e.g. consumer products)
Other Applications are in performance or power critical markets (e.g. military, medical)
It not that we just want it to work but we want it to work under tight constraints
Cannot depend on Moore’s Law to save you in the long run, it has to perform from day one

## Slide 26: Embedded Systems vs Regular Platform Design
Embedded devices are generally application specific. Embedded systems are made to do one thing or one related set of things.
Unlike desktop, laptop computers which can run any type of program or pretty good doing any type of program.
When you know that the device is gonna do one thing, you design it for the one thing, you don't design it for everything.
A general purpose machine is overpowered.
But embedded systems are designed specifically and they let you change the way you do design, you can just put in the things that you need to put in. Spend money on what you need to put in. So, higher design efficiency is possible in Embedded System.
In embedded system you have understand both the software and hardware, which makes it more difficult.
Notes: Watch 05 Embedded System Design

## Slide 27: Embedded Systems Structure
Sensors
Microcontroller
Actuators
Receives data from the outside world
Data
Data

## Slide 28: Microcontrollers
Integrated circuits that executes a program
Microcontrollers vs Microprocessors
Slower, 16 MHz - 500 MHz
Less memory, fewer features
Much cheaper
You write your program on computer, compile it and upload it to the flash memory of the microcontroller. As soon as there is power it runs the program.
We will use C to program microcontrollers

## Slide 29: Sensors
Sensors just receive information from the environment.
Thermistor: Receives temperature information.
Photoresistor: It reports light intensity.
CMOS camera (digital camera): It captures images

## Slide 30: Actuators
Actuators cause events to occur in the environment.
LEDs (light emitting diodes): they turn lights off and on
LCDs (liquid crystal displays): like what's on my digital watch
Servo motor: motors

## Slide 31: Analog to Digital Conversion
Converts Analog Data to Digital Data
Used to interface with analog sensors
Analog to digital is the same as the difference between real numbers and integers
So the universe. The world in general to the perception of humans is analog.
Digital phenomena is something that's either off or on, or at least has some discrete number of states.
In order for our program on our microcontroller to be able to use information from sensors, that analog signal has to be converted to a digital value.
Now on the output end, you usually need digital to analog conversion. So let's say I have a microcontroller and it's outputting some sound to some speakers. These speakers are analog devices, they need analog signal.
Notes: Watch 06 Analog to Digital

## Slide 32: Microcontroller Characteristics
Architecture (ARM, ESP32)
Datapath bitwidth (4 - 128 bits)
Number of bits in each registry
Determine accuracy and data throughput
Input/Output pins
Need enough pins to support the application
Performance
The clock rates are slower than desktops
Notes: Watch 07 microcontroller characteristics

## Slide 33: Other Microcontroller Characteristics
Timers
Needed for real-time applications
Analog to Digital Convertors
Used to read input from analog sensors
Low power modes
Power saving is key
Communication protocol support
Interface with other IC’s
UART, I2C, SPI, etc.

## Slide 34: IoT Devices are a Window to Cloud Services
Google Assistant and Alexa (processing is done on the cloud)
Netflix (Movie is not sitting on your phone but are in the cloud)
IoT devices give access to huge databases and computation resources on the cloud

## Slide 35: IoT involves two essential components
A device-side (made up of individual devices) that acts as a data source
A cloud-side that gathers data and provides resources for analyzing it

## Slide 36: Example: Water Pricing During Summer
Notes: An Example
Perhaps the best way to understand an IoT solution is to look at how one might be used in a true-to-life scenario. The specifics of this example are fictional but it should illustrate how the technology could be used. For more scenarios,see the list the IEEE is compiling here.
The Scenario
Suppose a small town is trying to figure out how to price water during the summer months. They want the town to look nice and enable people to keep their lawns green but they also don't want people wasting water which is in shorter supply during the summer. The town's officials need data to determine how often people actually need to water their lawns to keep them green and will use those data to help inform what price they should put on water usage during the summer.
The IoT Solution
The Devices
In order to collect they data they need, the town's officials select 100 houses at random across the town and ask them to install a small water sensor in their lawns that will detect the amount of moisture in the soil and send that data over the home's Wi-Fi connection to a central cloud service that will collect and store the data. The devices have the following requirements:
They must be small and unobtrusive.
They must be able to connect to Wi-Fi and be monitored by the home owner.
They must be battery operated and be able to run for 6 months without needing a new battery.
They must be able to detect moisture in the soil in percent saturation.
Must be able to store data for a 24-hour period in case the connection with the Wi-Fi router is lost.
Must be able to provide a rudimentary failure signal.
There could be a lot of other device requirements but these are the basics the device must contain. City engineers visit each house that has agreed to install the sensor, places the device in the yard at an optimal location, connects the device to the home's Wi-Fi router, and tests the connection with the cloud service.
The Data
The devices are programmed to collect moisture data every hour for a 24 hour period and average the readings to form a single number that is sent to the cloud service for storage. The dataset includes the device ID, the GPS location, a time/date stamp, and other relevant metadata.
The Cloud Service
City engineers developed a cloud-based solution to listen for incoming data from each device and collect that data in a database. The cloud service also listens for failure signals and can alert city engineers of an actual or pending device failure. The cloud services include an IoT gateway that handles communication with the devices, a storage solution to store the data, stream analytics service to manage the data coming in from the devices and an analytic services to analyze the data and inform decision making.
Analytics and Assessment
In our scenario, the town officials may use this data to understand better how often people actually are watering their lawns, how much they need to and make recommendations both to homeowners as well as policy makers about water usage and costs. Since weather is variable, the city engineers may need to collect data for many months to get accurate and actionable data. But the first step always is to collect the data in the first place and that's the power of IoT.

## Slide 37: Categories of IoT devices and services: Maker IoT
The term "maker" has come to be equated with “hobbyist” and refers to those who like to build things to experiment or for personal use out of electronic components. When it comes to IoT, the idea of building unpolished but functional devices that collect data, using cloud services to gather and store that data, and maybe even doing analytics on the data collected all is a part of what is included in this category. But a commercial business may employ a maker's approach to experiment with ideas, create proof-of-concept devices, do costing, and other planning exercises. So "maker" need not be limited to hobbyists but describes an approach to development.
Notes: “Maker” IoT. The term "maker" has come to be equated with “hobbyist” and refers to those who like to build things to experiment or for personal use out of electronic components. When it comes to IoT, the idea of building unpolished but functional devices that collect data, using cloud services to gather and store that data, and maybe even doing analytics on the data collected all is a part of what is included in this category. But a commercial business may employ a maker's approach to experiment with ideas, create proof-of-concept devices, do costing, and other planning exercises. So "maker" need not be limited to hobbyists but describes an approach to development.
Consumer IoT. As we'll see in the next topic, consumer IoT largely consists of commercial devices and associated services that are geared towards home or personal use such as connected thermostats or appliances. While the basic IoT concepts apply, the scope of what the devices collect, how they manage and store data, and how the data is used may be much more limited than what you'd find in an enterprise environment.
Enterprise IoT. Whereas Consumer IoT is focused on “turnkey” device solutions that solve specific problems or enable new scenarios for individuals or homes, enterprise-class IoT is focused on solving specific business problems like efficiency, reducing waste, increasing speed to market or of production, and providing intelligence on how business systems are running. A single enterprise may deploy dozens of devices that work in concert to give a business a single view of a factory or fleet of planes or gas pipeline. Enterprises also may require real-time data and real-time analysis of those data in order to make just-in-time adjustments or prevent disastrous consequences from a failed system. Consumer-grade IoT products rarely require this so the type of architecture needed in an enterprise will be more involved and require more services than a consumer solution requires.

## Slide 38: Consumer IOT
It largely consists of commercial devices and associated services that are geared towards home or personal use such as connected thermostats or appliances. While the basic IoT concepts apply, the scope of what the devices collect, how they manage and store data, and how the data is used may be much more limited than what you'd find in an enterprise environment.

## Slide 39: Enterprise IoT
Whereas Consumer IoT is focused on “turnkey” device solutions that solve specific problems or enable new scenarios for individuals or homes, enterprise-class IoT is focused on solving specific business problems like efficiency, reducing waste, increasing speed to market or of production, and providing intelligence on how business systems are running. A single enterprise may deploy dozens of devices that work in concert to give a business a single view of a factory or fleet of planes or gas pipeline. Enterprises also may require real-time data and real-time analysis of those data in order to make just-in-time adjustments or prevent disastrous consequences from a failed system. Consumer-grade IoT products rarely require this so the type of architecture needed in an enterprise will be more involved and require more services than a consumer solution requires.

## Slide 40: IoBT, Software and Combat Clouds
Internet of battlefield things (IoBT) - Military planners envision a future battlefield defined by the internet of things, one in which smart devices, soldier-worn sensors and unmanned aircraft produce a nonstop torrent of actionable data.
Software defined aircraft - All revealed fifth-generation fighters use commercial off-the-shelf main processors to directly control all sensors to form a consolidated view of the battlespace with both onboard and networked sensors.
Combat clouds - Fifth-generation jet fighters will operate together in a "combat cloud" along with future unmanned combat aircraft.
Notes: https://www.c4isrnet.com/special-reports/military-it-modernization/2018/08/03/the-internet-of-things-will-depend-on-modernized-networks/
https://www.c4isrnet.com/opinion/2018/10/03/the-internet-of-battlefield-things-is-coming-are-it-pros-ready/
https://en.wikipedia.org/wiki/Fifth-generation_jet_fighter

## Slide 41: An IoT Device
Connected to the Internet
Secure
Smart Features
Communication Capabilities with other devices
Remotely Configurable
Programmable
Replaceable (Optional)
Environmentally Flexible (Optional)
Notes: An IoT Device
Here are some criteria that a device should meet to be considered an IoT device. Many of these properties are defined in the IEEE white paper on IoT and confirmed from other sources.
Connected to the Internet. The most obvious criterion is that the device has a connection to the internet with a unique identifier, and two-way communication. Both of these properties are important for a device to be considered a part of an IoT system. The device has to be unique to ensure secure communications with both the server and with other devices and the device has to be able to consume and deliver data. A primary value proposition for IoT is data collection as well as consumption.
Secure. Being able to uniquely identify a device on the internet or within an IoT ecosystem is one aspect of security but making a device secure also means it's resistant to being hacked (both the hardware and software), uses encrypted communication protocols, and is immune to mimicry either by an alternate hardware device or a virtual device.
Smart Features. This simply means that the device must have sensors or hardware that enable it to collect specific data based on events (like smoke in the air or a light being switched on or a key being turned). There is an implication that the device should be able to do this without user interaction so it has an “embedded intelligence.”
Communication Capabilities. The device should have the capability to communicate not only with cloud-based services but with other devices.
Configurable. The device should be remotely configurable or have the ability to self-adjust its configuration based on changes in the ecosystem. This includes the ability to automatically install updates, modify sensor receptivity, repair problems, and modify energy consumption among others.
Programmable. Like connectivity to the Internet, this should be a basic function of any connected device but certainly is true of IoT devices. The main idea here is that the function of the device should be able to be modified without having to make changes to its hardware. This may mean that a device has a number of sensors that could be activated or deactivated by software or, if a single-purpose device, the features should be able to be modified by software to accomplish a different task (for example, a thermostat that can deliver outside temperature readings from a service vs. taking the internal temperature readings from a sensor).
These probably wouldn't be considered “core” features but here are other properties to consider when defining a device as an "IoT device."
Replaceable. In many scenarios, when an IoT device fails (for example, a sensor on an airplane engine or wind turbine), the device should be able to be replaced and it's entire firmware and software settings loaded onto the device quickly and easily. This could mean that every programmable feature of the device should be able to be stored in the cloud and downloaded to a replacement device.
Environmentally Flexible. Depending on the scenario, the device should be able to maintain power, collect and store data, and smartly upload stored data in the event of a power outage, and/or loss of Internet connectivity.
https://iot.ieee.org/images/files/pdf/IEEE_IoT_Towards_Definition_Internet_of_Things_Revision1_27MAY15.pdf

## Slide 42: Consumer versus Business Goals for IoT
Individual consumers implement cloud connected devices (such as doorbells, thermostats, and even refrigerators) in order to make their life easier, more comfortable, or more secure. Consumer devices in the home are not typically being used for the same purpose as an IoT device implemented in a business scenario.
In a way, business goals for IoT are simple compared with consumer goals. Businesses tend to implement IoT solutions in order to be more profitable, to increase safety for their work force, and to more easily comply with government regulations in order to create a better business environment. Profitability can be realized either directly through cost reductions or indirectly through competitive advantage. A business could use IoT to provide customers with improved service, resulting in increased market share (and overall profits). In most cases both the business and their customer benefit.

## Slide 43: IoT Consumer Space Examples
Connected Refrigerators
Connected Doorbells and Cameras
Connected Thermostats
Notes: While IoT in the consumer space is still fairly nascent, there regularly are new examples of the technology being used to improve customer experiences and expand product features. Here are a few scenarios (some with which you may already be familar):
Connected Refrigerators. The Samsung “Family Hub” line of refrigerators includes a large, touch screen that enables customers to more easily track their food inventory through the use of interior, web-enabled cameras, an easy-to-use shopping list, calendaring and TV mirroring features. While the element of data collection and analysis isn't central to this IoT solution, the refrigerator is an early look at the potential for connected appliances.
Connected Doorbells and Cameras. Many companies have gotten into the consumer doorbell and camera business. The Ring system and Google's Nest Hello device are examples. These doorbells record and store video and enable two-way voice and one-way video calling for people at the door. The Nest device will do facial recognition and use AI to determine which type of object it detects (car, person, animal).
Connected Thermostats. As we mentioned earlier, the connected thermostat is probably the most widely-used example of an IoT consumer device most likely because it was one of the first connected devices to check all the boxes in terms of using an IoT architecture. The most famous device is the Nest Thermostat but there are others. Microsoft recently released its GLAS thermostat in partnership with Johnson Controls and Honeywell has a line of connected thermostats. These devices enable customers to view and control their indoor temperature anywhere using a mobile device and an internet connection, set a heating and cooling schedule, view historical data on their home's temperature and energy consumption, and even get alerts when their heater's filter needs to be changed.
There are many other connected devices coming to market, that range from practical to weird. But the possibilities are nearly endless. Consumers are moving from a mindset of experimentation to anticipation that will soon evolve into expectation as connected devices enable customers to do more.

## Slide 44: Business goals for IoT, improving:
Product Quality and Extended Product Lifetime
Service Reliability and Uptime
Operating Efficiency
Workforce safety
Governmental compliance
Notes: Business goals for IoT focus on improvement in one or more of the following areas:
Product Quality and Extended Product Lifetime
Service Reliability and Uptime
Operating Efficiency
Workforce safety
Governmental compliance

## Slide 45: IoT Verticals
Manufacturing
Smart City
Smart Building
Healthcare
Energy
Transportation and Smart Vehicles
Logistics and Inventory Management
Retail
Agriculture
Military
Notes: IoT Business Scenarios
Bookmark this page
In this lesson, you will explore the ways that different businesses/industries (often referred to as “verticals” by industry experts to denote the depth of a solution rather than it's breadth) implement IoT solutions. Each vertical has their own specific needs and problems that must be addressed, so the IoT implementation within a vertical is often customized in some manner to address their requirements. Of course, there is a significant overlap between verticals, it's important to think through the needs of the industry for which you are creating an IoT solution.
As you might imagine, IoT can be implemented in both small and large businesses, and in nearly any type of business as well. Some of the industry verticals that have a high adoption rate are listed below. We won't be exploring all of theses verticals during this course, but we have selected a few that demonstrate the different approaches that may be applied by businesses within a vertical during the design and implementation of an IoT solution.
Manufacturing
Smart City
Smart Building
Healthcare
Energy
Transportation and Smart Vehicles
Logistics and Inventory Management
Retail
Agriculture

## Slide 46: IoT Sub-systems Description
Cloud Gateway: The Cloud Gateway provides a cloud hub for secure connectivity, telemetry and event ingestion and device management (including command and control) capabilities.
Stream Processing: Processes large streams of data records and evaluates rules for those streams.
Business Process Integration: Facilitates executing actions based on insights garnered from device telemetry data during stream processing. Integration could include storage of informational messages, alarms, sending email or SMS, integration with CRM, and more.
Storage: Storage can be divided into warm path (data that is required to be available for reporting and visualization immediately from devices), and cold path (data that is stored longer term and used for batch processing).
User Interface: The user interface for an IoT application can be delivered on a wide array of device types, in native applications, and browsers.

## Slide 48: Example of Sensors Available
Temperature
Humidity
Energy
Compass
Pressure
Sonar
Light and UV

## Slide 49: Edge Computing
Edge computing is a distributed computing paradigm which brings computer data processing and storage closer to the location where it is needed. So, instead of having a centralized, remote cloud to do all the work, the data is handled and stored locally, i.e. on the IoT device itself or at the nearest network node.
Computation is largely or completely performed on distributed device nodes.
Edge computing pushes applications, data and computing power (services) away from centralized points to locations closer to the user.
Edge computing does not need contact with any centralized cloud, although it may interact with one.
Edge application services reduce the volumes of data that must be moved, the consequent traffic, and the distance the data must travel. That provides lower latency and reduces transmission costs.
Notes: https://en.wikipedia.org/wiki/Edge_computing

## Slide 50: Why pure cloud computing isn’t the best option for IoT
Traditional cloud computing has a number of drawbacks when it comes to IoT:
Data security threats. Data is constantly being transmitted back and forth between the cloud and a device, and as such, the risk of privacy violation is heightened.
Performance issues. IoT applications rely heavily on real-time actions. Yet, the processing speed of your cloud-based app often depends on the actual distance between the device itself and the server location.
Operational costs coincidentally grow as the amount of data produced and shared increases.
On top of that, most data sourced to the cloud often bears no practical value and is never used.
Notes: https://easternpeak.com/blog/the-impact-of-edge-computing-on-iot-the-main-benefits-and-real-life-use-cases/

## Slide 51: How does edge computing work?
Every IoT sensor produces tons of data every second. In the case of cloud computing, the data is instantly transferred to the central, unified cloud database where it’s processed and stored.
If there’s any action required, the central server will send its response back to the device upon receiving and analyzing the acquired data.
While the whole process typically takes less than a second to complete, there might be situations when the response may be delayed or interrupted. This can happen due to a network glitch, weak internet connection, or simply because the data center is located too far from the device.
Now, in case of edge computing, you don’t need to send the data acquired by the IoT sensors anywhere. The device itself or the nearest network node (e.g. the router) is responsible for data processing and can respond in a proper manner if action is required.

## Slide 52: Edge Computing makes it possible that the IoT device is no longer dependent on the internet connection and can function as a standalone network node.

## Slide 53: The benefits for edge computing in IoT
Increased data security
Better app performance
Reduced operational costs
Improved business efficiency and reliability
Unlimited scalability
Notes: The benefits for edge computing in IoT
As you can see, the main purpose of edge computing is to decentralize data handling. This leads to a number of advantages over the traditional cloud.
Namely, there are 5 main advantages of edge computing for IoT:
1.Increased data security
While IoT solutions represent a perfect target for cyber attacks, edge computing can help you secure your networks and improve overall data privacy.
Because the data is decentralized, distributed among the devices where it is produced, it’s difficult to take down the whole network or compromise all of the data with a single attack.
This approach is also preferred in terms of GDPR compliance: the less sensitive information is sent through your network and stored in your cloud, the better.
2. Better app performance
As mentioned above, it takes some time for the data travel back and forth between the device and the data center.
By storing and processing the data close to its source, you reduce the lag time and improve the overall app performance. As a result, you can analyze the data in real-time, without delays.
3. Reduced operational costs
When you store and process most of the data “at the edge”, you don’t need an abundance of cloud storage. Plus, you can filter out the unnecessary information and backup only the relevant data.
As a result, your infrastructure costs will inevitably go down.
4. Improved business efficiency and reliability
Lower data traffic and reduced cloud storage, in turn, lead to more efficient business operations.
Additionally, connection issues won’t be extremely problematic as they are for other IoT products that rely on the cloud. This is due to the fact that your devices can work autonomously, without internet connection.
5. Unlimited scalability
Unlike cloud, edge computing allows you to scale your IoT network as needed, without reference to the available storage (or its costs).
As a result of the listed benefits, edge computing really shines when it comes to time-sensitive tasks.

## Slide 54: Edge Computing Use Cases
McKinsey finds that the industries with the most edge computing use cases are:
travel, transportation, and logistics
energy
retail
healthcare
utilities

## Slide 55: Voice Revolution

## Slide 56: Voice control is most suitable in the following IoT use cases
Home automation
Automobiles
Health Care
Entertainment
Notes: https://www.zeolearn.com/magazine/how-is-voice-recognition-affect-iot

## Slide 57: Voice Assistants Are Taking Over Consumer IoT
No industry felt the heat of the voice assistant battle more than Consumer IoT (CIoT), in which voice assistant integrations became the primary focus for any CIoT product-centric company.
Imagine a future in which every command is at the tip of your tongue. When you wake up. your bathroom mirror can report your schedule for the day. During breakfast, you can ask the coffee machine for a latte, extra foam. On the train, your watch will tell you just how late you’ll be to work. In the office, your printer will pipe up, asking for more ink, please.
Notes: https://www.iotforall.com/voice-assistants-consumer-iot/

## Slide 58: Entry point into the IoT’s has been Amazon and Google’s smart speakers
For many consumers, the entry point into the Internet of Things has been Amazon and Google’s smart speakers.
Voice control is one of the primary drivers of smart home market growth with the number of home voice devices projected to reach 275 million by 2023 in USA alone.

## Slide 59: Visions of dialogue from science fiction
Hal “2001: A Space Odyssey” (1968)
  Naturally conversing computer
Star Trek (original 1966)
  Natural language command and control
Her (2013)
  A virtual partner with natural dialogue capabilities

## Slide 60: A NEW KIND OF UI: VUI

## Slide 63: Technology revolutions
1456
1765
1943
1981
1994
2008
2014
2016

## Slide 66: What is a Bot?
A Bot is a conversation based UI
Conversation is based on language
Conversation takes place on a general canvas
Canvas can be: Chat Client: Skype, Team, Slack, Messenger Voice: Echo, Cortana Skills, Siri, Google Now App: Website, App

## Slide 67: Scenario’s for Bots
Question and Answers
Automate Helpdesk, Handoff to human if too complex
Product selection and ordering
Task Automation
Proactive Assistance & Monitoring
Expert Systems

## Slide 68: Bot Examples

## Slide 69: Embedded devices with dialogue capabilities
Amazon Echo (2014) – home assistant device
  Plays music
    With voice commands
  Question answering
    Get weather, news
    More complex questions, like
      “how many spoons are in a cup?”
  Setting timer
  Manages TODO lists

## Slide 70: Embedded devices with dialogue capabilities
Answers questions
Sets time
Device control and queries.
Thermostat Etc.

## Slide 71: Dialogs are for bots like screens are for apps
  They separate concerns and organize flows, exactly the same way:
Traditional Application
Main Screen
New Order Screen
Product Search Screen
Bot
Root Dialog
New Order Dialog
Product Search Dialog

## Slide 74: Google Assistant coming soon to more speakers, appliances and other devices
Google is putting its Assistant on a wide range of third-party hardware. Google has announced that it’s going to be putting the Assistant on partner speakers, appliances, connected cameras, and much more.
It is already on the iPhone.

## Slide 75: Google wants to ‘see’ as well as ‘hear’ your surroundings

## Slide 76: How to develop for the Google Assistant platform

## Slide 77: Actions on Google https://developers.google.com/actions/
Actions on Google is a developer platform that lets you create software to extend the functionality of the Google Assistant, Google’s virtual personal assistant, across more than 500 million devices, including smart speakers, phones, cars, TVs, headphones, watches, and more.
You can build smart home Actions that let users control Internet of Things (IoT) devices through the Google Assistant. Building smart home Actions lets you connect, query, and control devices through your existing cloud infrastructure.

## Slide 78: Messaging Protocols: Kafka and MQTT
MQTT is a publish/subscribe protocol particularly suited to IoT applications thanks to its small footprint, real-time guarantees, and suitability for use in high-latency, low-throughput, and unreliable networks. It is designed for connections with remote locations where a "small code footprint" is required or the network bandwidth is limited. The publish-subscribe messaging pattern requires a message broker.
Based on a publish/subscribe model, Kafka is one of the most widely used platforms to process and distribute real-time data streams. It is used for building real-time data pipelines and streaming apps. It is horizontally scalable, fault-tolerant, wicked fast, and runs in production in thousands of companies.
Both, MQTT and Apache Kafka have great benefits for their own use cases. But, none of them are the single allrounder for everything. The combination of both makes them very powerful and a great solution to build IoT end-to-end scenarios from the edge to data center and back.
Notes: Read: https://dzone.com/articles/apache-kafka-mqtt-end-to-end-iot-integration-githu
https://thenewstack.io/apache-kafka-cornerstone-iot-data-platform/

## Slide 79: The future of IoT is AI
As IoT devices will generate vast amounts of data, then AI will be functionally necessary to deal with these huge volumes if we’re to have any chance of making sense of the data.
Data is only useful if it creates an action. To make data actionable, it needs to be supplemented with context and creativity. IoT and AI together is this context, i.e. ‘connected intelligence’ and not just connected devices.
Traditional methods of analysing structured data and creating action are not designed to efficiently process the vast amounts of real-time data that stream from IoT devices. This is where AI-based analysis and response becomes critical for extracting optimal value from that data.
Notes: https://www.techuk.org/insights/opinions/item/13827-the-future-of-iot-is-ai
https://www.wired.com/brandlab/2018/05/bringing-power-ai-internet-things/

## Slide 80: Blockchain in the Internet of Things?
Traditional IoT systems are dependent on a centralized architecture. Information is sent from the device to the cloud where the data is processed using analytics and then sent back to the IoT devices.
With billions of devices set to join IoT networks in the coming years, this type of centralized system has very limited scalability, exposes billions of weak points that compromise network security and will become incredibly expensive and slow if third-parties have to constantly check and authenticate each and every micro-transaction between devices.
Smart contracts in blockchain networks will allow devices to function securely and autonomously by creating agreements that are only executed upon completion of specific requirements. It not only allows for greater automation, scalability and cheaper transfers (no third-party needed to oversee transactions).
With traditional centralized networks, the risk of a single point of failure disabling an entire network is a very real possibility. A decentralized blockchain network mitigates this risk with millions of individual nodes that transfer data on a peer-to-peer (p2p) basis to keep the rest of the IoT network running smoothly.
Notes: https://cointelegraph.com/news/how-significant-is-blockchain-in-internet-of-things

## Slide 81: IoT and Blockchain Complement Each Other
Blockchain technology can be used in tracking billions of connected devices, enable the processing of transactions and coordination between devices; allow for significant savings to IoT industry manufacturers. ... In an IoT network, the blockchain can keep an immutable record of the history of smart devices.

## Slide 82: IoT + Cloud and Edge Computing + AI + Blockchain: The Fourth Industrial Revolution has Begun
The combination of IoT, Cloud and Edge Computing, AI and Blockchain technologies allow machines in the Internet of Things to be able to lease themselves out, schedule and pay for their own maintenance, purchase their own replacement parts and keep their own transactional records, using blockchain.